## Slide 1
[command]
move / pause / resume
set variables
[map, locations]
(not yet) (?)
[command]
pause / resume
[map, locations]
(not yet)
FMS
UI
SLAM
Websocket
LCM
데이터 전송

## Slide 2
[MAP_DATA](test)
map / locations
[ROBOT_STATUS]
cur pose
cur path
state / battery
err_code
[ROBOT_STATUS]
cur pose
cur path
state / battery
err_code
[MAP_DATA]
(not yet)
FMS
UI
SLAM
Websocket
LCM
데이터 전송

## Slide 3
robot state (int8) | 
VALUE | MEAN
0 | not ready (not connected, initializing)
1 | ready (move done; move stopped)
2 | moving
3 | avoiding
4 | paused
5 | error (collision, motor error, ..)
6 | manual mode
err_code (int8) | 
VALUE | MEAN
0 | no error
1 | collision error
2 | no path error
3 | motor comm error
4 | motor error
5 | voltage error
6 | sensor error
공통으로 사용하는 변수 정의
필요 시, 변경 및 추가 가능합니다. (상세 정의 필요)

## Slide 4
FMS
UI
Websocket
JSON
Name | Type | Ex
msg_type | string | “COMMAND”
cmd | string | “PAUSE” “RESUME”
Name | Type | Ex
msg_type | string | “MAP_DATA”
map_name | string | “rainbow_test”
map | array | (size = 1)
len | int | 1000000 (width*height pixel)
width | int | 1000 [pixel]
height | int | 1000 [pixel]
data | string | Bytearray to string
grid_width | float | 0.025 [m]
origin_x | int | 500 [pixel]
origin_y | int | 500 [pixel]
location | array | (size = location number)
name | string | “CHARGE” “WAIT” “TABLE_1” “TABLE_2”
x | float | 0.5 [m]
y | float | -1 [m]
th | float | PI/2 [radian]

## Slide 5
FMS
UI
Websocket
JSON
Name | Type | Ex
msg_type | string | “ROBOT_STATUS”
robot_name | string | “rainbow1”
state | string | “NOT_READY” “READY” “MOVING” “AVOIDING” “PAUSED” “ERROR”
battery | float | 54.2 [V]
err_code | int | 0 : no error 1 : collision error 2 : no path error 3 : communication error …
cur_pose | array | (size = 1)
x | float | 1 [m]
y | float | -0.5 [m]
th | float | 0 [rad]
cur_path | array | (size = path number)
x | float | 
y | float | 
th | float | 
Name | Type | Ex
msg_type | string | “SET_MAP”
map_name | string | “rainbow_test”
len | int | 1000000 (width*height pixel)
width | int | 1000 [pixel]
height | int | 1000 [pixel]
data | string | Bytearray to string
grid_width | float | 0.025 [m]
origin_x | int | 500 [pixel]
origin_y | int | 500 [pixel]
Name | Type | Ex
msg_type | string | “REQUEST_MAP”

## Slide 6
UI
SLAM
LCM
“COMMAND” |  | 
Name | Type | Ex
cmd | int32_t | 1 : move location 2 : move target 3 : move joystick (계속 보냄) 4 : move manual (수동으로 미는 모드) 5 : move stop 6 : pause 7 : resume 8 : set variable 9 : request map (임시-테스트용)
params | byte[255] | (별도 표 참고, 표에 없으면 param 안씀)
cmd | 1 | 2 | 3 | 8
0 | location num 1 : charge 2 : wait point 3 ~ : tables | x | vx (-1.0 ~ 1.0) | variable 1 : velocity x,y 2 : velocity 소
1 |  |  |  | value (0 ~ 1.0(max))
2 |  |  |  | 
3 |  |  |  | 
4 |  | y | vy (1.0 ~ 1.0) | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
8 |  | th | vth (-1.0 ~ 1.0) | 
9 |  |  |  | 
10 |  |  |  | 
11 |  |  |  | 
12 |  |  |  | 
13 |  |  |  | 
14 |  |  |  | 

## Slide 7
UI
SLAM
LCM
“MAP_DATA” |  | 
(request 하면 1회 보냄) |  | 
Name | Type | Ex
map_name | string | 
grid_width | double | 
width | int32_t | 
height | int32_t | 
origin | int32_t [2] | 
len | int32_t | 
data | byte [len] | 
loc_num | int32_t | 
loc_name | string [loc_num] | 
loc_pos | double [loc_num][3] | 
“ROBOT_STATUS” |  | 
(주기 : 200ms (?) AFAP) |  | 
Name | Type | Ex
battery | double | 
state | int8_t | 0 : not ready 1 : ready 2 : moving 3 : paused 4 : avoiding 5 : error
err_code | int8_t | 0 : no error 1 : collision error 2 : no path error 3 : communication error …
cur_x | double | 
cur_y | double | 
cur_th | double | 
path_num | int32_t | 
path_x | double [path_num] | 
path_y | double [path_num] | 
path_th | double [path_num] |